## Slide 1: Plant Nurture System
sddec24-16
Cameron Jones, Blake Hardy, Cayden Kelley, Chase O’Connell, Holden Brown, Tejal Devshetwar
Advisor: Ahamed, Md Maruf

## Slide 2: Project Overview
Create a device that automatically collects soil data (NPK,moisture,temperature).
Sends the data to a database on a server.
Create a mobile app which presents the collected data to the users.
Server has logic that sends commands to automatically water/fertilize plants when certain conditions are met.

## Slide 3: Detailed Design and Visuals
Overall:
Data from sensors are transferred to Microcontroller.
Data from microcontroller transferred to database which in then is displayed on the app.
Database returns commands to actuate water pump.

## Slide 4: Detailed Design and Visuals
App:
The temperature, UV Index, Humidity are obtained through API and updated based on current location.
Each card opens up detailed information about each plant.

## Slide 5
Nitrogen, Phosphorus, and Potassium Sensor
RS485 to UART converter
Soil Moisture & Temp. Sensor
Water Pumps
Relays
Ground
12 V Power
3.3 V Power
Pico Power Out
Switched 3.3V
Communication

## Slide 6: Functionality: System Overview
Mobile App: Central hub for user interaction and data visualization.
Sensor System: Monitors nutrients, storing data in the cloud.
Actuators: Automatically dispense nutrients based on plant needs.
Water actuator dispensing
Mobile app view of user created plants

## Slide 7: Functionality: Key Features
Multiple Plants and Sensors: Manage several plants and corresponding sensors.
Plant Profiles: Create a unique profile for each plant.
Automated Nutrient Dispensing: Actuators respond to sensor data, ensuring optimal plant health.
Mobile app view of user created plants
Water actuator dispensing

## Slide 8: Functionality: Key Features
Data-Driven Insights:
  Real-time monitoring of sensor data.
  Graphical representation of sensor data for easy interpretation.
Smart Notifications:
  Reminders and alerts tailored to each plant's care schedule.
  Explanation of sensor metrics.
User tapping PAR and receiving a detailed explanation

## Slide 9: Technology Considerations
Raspberry pi pico w
  Small form factor
  Low power and heat
  Wireless communication
  Sufficient IO capability
  Good software support
AWS server
  Ease of use
  Low cost
I2c sensors
  Simple
  Easy part availability
  Low component cost
Rs485 sensors
  Limited choices
  Good hardware and software support
Notes: Compute power is not a concern with this device. All its doing it getting sensor data and relaying it to a server. Anything with more compute is not necessary, the pico is already overkill. In theory it does allow us to implement advanced features a more minimalist microcontroller would not. Not that we plan to. The pico is also much cheaper than a regular pi Heat is a problem in an enclosed space and adding a cooling solution would make waterproofing much more difficult. AWS because its free up to a certain threshold which we probably will not hit. I2c cause its everywhere, modbus cause we dont have a choice but its not too difficult to work with. Ideally we would be using more and higher quality sensors, but those are expensive.

## Slide 10: Areas of Concern and Development
Satisfying Requirements
  Successful calibration per plant
  Effectiveness of auto-fertilization
Meeting User Needs
  Hobbyist level peripherals (Budget)
  Limited precision
  Quality required for research an industry
  Appearance & Form Factor
  Benefit over manual care
Potential Change in Scope

## Slide 11: Conclusions
Key Components:
  App
  Server Communications
  Device (Sensors, Actuators)
Technology Selection
  Raspberry Pi Pico
  I2C Sensors
  RS485 Sensors
Areas of Concern
  Quality and Precision
  User-base

## Slide 12: Questions?